## Slide 1
TRAPNET - Viva Defense and Technical Questions Working Principles, Sensor Mechanics and Examiner Q&A

## Slide 2
Sensor Physics: mmWave Radar and Wall Penetration
Parameter / Feature | Technical Explanation and Operational Physics
Detection Mechanism (LD2410C 24GHz FMCW) | Operates on 24GHz Frequency Modulated Continuous Wave (FMCW) radar. Emits high-frequency radio waves and measures frequency shifts (Doppler Effect) of reflected signals. Micro-Doppler sensing detects 3-5mm chest breathing displacement of stationary hidden humans.
Wall and Barrier Penetration (Electromagnetic Attenuation) | 24GHz radio waves penetrate non-conductive, low-density materials (drywall, wood, glass, plastic, thin brick) due to low dielectric attenuation. Dense metals (steel, iron) reflect waves, acting as boundary shields.
Signal Processing and Gate Thresholds | Signal energy is digitized across motion and static gates (0.75m to 6m range). Human presence is validated when static energy exceeds Gate Energy > 40 on ESP32-S3 via UART (256000 baud).

## Slide 3
Actuation and Sensing: Vibration Sensor and Relay Control
Component / Module | Working Principle, Circuit Connection and Signal Reaction
SW-420 Vibration Sensor (Intracavity Shock Detection) | Suspended metallic spring inside conductive cylinder. Mechanical shock causes spring contact (LOW pulses). Noise Filtering: Potentiometer thresholding + software pulse counting (>15 pulses/500ms = forced entry; single transient truck shocks rejected). Connected to GPIO34/39 with mandatory 10kohm pull-down.
2-Channel Relay Module (Galvanic Isolation) | Optocoupler barrier isolates 3.3V/5V ESP32-S3 logic from high-current 12V solenoid lock, preventing inductive kickback damage. Active-LOW trigger: ESP32 pulls GPIO32 LOW -> optocoupler fires -> relay coil energizes -> NO contacts close -> 12V locks door (<3s).
IR Sensors (FC-51 / HW-201) (Boundary Breach Guard) | Transmits 940nm infrared light. Door/window opening breaks light beam or causes reflection drop, driving GPIO4/13 LOW in <1ms for zero-latency boundary breach detection.

## Slide 4
Alert Infrastructure: SIM800L and Multi-Layer SOS
Alert Channel / Module | Communication Mechanism and Power Architecture
SIM800L GSM Communication (Cellular SMS Transceiver) | Communicates with 2G cell towers via AT commands over UART (9600 baud). Dispatches SMS with breach timestamp and GPS coordinates. Power: Requires dedicated 4.0V buck rail + 1000uF cap to handle 2A peak current bursts without browning out ESP32-S3.
Proximity Beacons (WiFi Beacon and BLE Eddystone) | WiFi Beacon: ESP32-S3 broadcasts unencrypted AP SSID ('SOS_INTRUDER_TRAPPED_GPS...') readable by any phone within 30m without app/pairing. BLE Eddystone: Broadcasts passive BLE telemetry packets (15m radius).
Device Mesh Relay (ESP-NOW Mesh Protocol) | 2.4GHz peer-to-peer connection reaching 200m+ to neighboring nodes without internet or WiFi router. Enables building-wide SOS relay in zero-connectivity environments.

## Slide 5
External Examiner Valuation: Key Viva Q&A (Part 1)
Examiner Question | Technical Viva Defense Response
Q1: Why mmWave radar over standard PIR motion sensors? | PIR only senses infrared changes of moving bodies. If an intruder stands still or hides behind obstacles, PIR fails. LD2410C 24GHz mmWave radar senses micro-Doppler chest breathing motion (3-5mm) of stationary humans through non-metallic walls.
Q2: How does the system handle power cuts or cut wires? | Main power comes from a 12V 2A adapter. Dual 18650 Li-Ion batteries (7.4V) with TP4056 protection provide 4-6 hours offline power backup. GSM SMS, local SD logging, and WiFi/BLE/ESP-NOW operate 100% offline without internet.
Q3: How do you prevent false alarms from pets or passing trucks? | Multi-sensor fusion: Radar static energy >40 AND vibration pulse count >15/500ms AND (on V2) YOLOv8 vision AI on RPi Zero 2W confirms human presence before solenoid door locks.

## Slide 6
External Examiner Valuation: Key Viva Q&A (Part 2)
Examiner Question | Technical Viva Defense Response
Q4: Why decoupling into ESP32-S3 and Raspberry Pi Zero 2W? | Decoupled Edge Architecture: ESP32-S3 handles hard real-time sensor processing (<500ms), relay locking (<3s), and radio beacons. RPi Zero 2W runs heavy vision AI (YOLOv8). Image processing latency never delays critical locking or emergency SOS.
Q5: Why a dedicated LM2596 buck converter for SIM800L? | SIM800L operates at 3.4V-4.4V and draws 2A peak current bursts during GSM transmission. Powering it from ESP32 lines causes voltage sags and resets. A dedicated 4.0V buck + 1000uF cap ensures voltage stability.
Q6: What is the disarm / safety mechanism for false locking? | The 12V solenoid lock is fail-secure via 2-channel relay. Authorized users can disarm via SMS disarm passcode sent to SIM800L or an emergency mechanical manual key override inside.