## Slide 1
Department of Electronics and Communication Engineering
Final Year Project — 2026-2027
TRAPNET
Design and Implementation of a Tamper-Resilient mm Wave-Radar-Based Intrusion Containment System with Mesh-Relayed SOS Alerts
Batch Reg No:
Mohamed Sameer F (43130597)
Raahul N (43130640)
Review Presentation
Guide Name:
Ms.S.Bhuvaneshwari, M.E.,
Assistant Professor, Department of ECE

## Slide 2
Introduction
TRAPNET — Autonomous Intruder Containment System
TRAPNET (Trapping Network) is an Edge-AI driven physical intrusion containment system
designed for small businesses, academic institutions, and residential security. Unlike
conventional CCTV systems that only record, TRAPNET actively responds to intrusion by
physically trapping the intruder and simultaneously triggering a resilient multi-layer SOS
alert.
Core Technology Stack:
mmWave Radar (HLK-LD2410 24GHz)
Detects 5mm chest breathing motion of stationary hidden intruder
YOLOv8 Vision AI (Raspberry Pi Zero 2W)
Camera-based person detection as secondary confirmation layer
Solenoid Door Lock (12V)
Physical containment: door locks in under 3 seconds upon confirmed detection
Multi-Layer SOS Alert
Wi Fi Beacon + BLE Eddystone + GSM SMS + ESP-NOW Mesh; operates with ZERO internet

## Slide 3
Objectives
1. To design and implement an autonomous physical intrusion containment system capable of detecting human presence and triggering door locking within 3 seconds of confirmed intrusion.
2. To integrate mmWave radar (HLK-LD2410, 24GHz) for reliable stationary-human detection by sensing 5mm micro-Doppler chest breathing signatures — overcoming the core failure of PIR sensors. To deploy YOLOv8 edge-AI on Raspberry Pi Zero 2W for camera-based person detection as a secondary sensor fusion layer, reducing false-positive rate and confirming intrusion before actuation.
3. To implement a 4-layer internet-independent SOS alert system (WiFi Beacon + BLE Eddystone + GSM SMS via SIM800L + ESP-NOW multi-hop mesh), resilient to WiFi jamming, power cuts, and connectivity loss.
4. To achieve full-system offline resilience using 18650 battery backup (4–6 hrs), MicroSD event logging, and GSM cellular communication — ensuring operation independent of internet infrastructure.

## Slide 4
Problem Statement
Why TRAPNET is Needed — The Security Gap
1. CCTV systems only RECORD — they never RESPOND. A thief walks in, steals, and walks out; the camera captures it all but does nothing to stop it.
2. PIR motion sensors MISS stationary intruders. A professional thief who freezes still goes completely undetected — a known and exploited vulnerability.
3. Camera tamper defeats the entire system. Spraying paint or placing a cloth over the camera causes security systems to lose their only detection channel.
4. Single-layer alerts fail under attack. WiFi jamming, internet outage, or power cut disables most IoT-based security systems in a single step.
5. No physical containment exists in affordable systems. High-cost commercial solutions exist, but no sub-₹8,000 system physically traps and alerts simultaneously.

## Slide 5
Existing Block Diagram

## Slide 6
Scope & Application
Deployment Area | Problem Addressed | TRAPNET Solution
Banks & ATMs | Unauthorized after-hours entry; vault tamper | mm Wave detects frozen intruder + solenoid lock + GSM silent alarm to security
Retail Shops & Warehouses | Night theft after shutter close; camera spray by thieves | Camera tamper = trigger; radar as backup; SMS to owner within 3 sec
Corporate Offices & Server Rooms | Restricted zone breach; insider threat; asset theft | ESP-NOW mesh alerts entire floor; vibration sensor detects locker drilling
Academic Labs & Libraries | Equipment theft; unauthorized equipment removal | GPS on asset sends live coordinates via GSM if moved; OLED live status HUD
Rural & Remote Locations | No internet; no GSM 4G coverage in some areas | GSM 2G SMS works on SIM800L; fully offline with battery backup 4-6 hours
Residential Security | Break-in through back door; no app or subscription | WiFi Beacon visible in nearby phones WiFi list — no app, no pairing needed

## Slide 7
Literature Summary
Sl. No | Author & Paper Title | Methodology | Learning / Finding | Future Enhancement
01 | Raimondi et al. (IEEE Sensors Journal, 2024) mmDetect — 60GHz FMCW Radar | Indoor human detection using 60GHz FMCW radar pipeline; energy thresholding on Doppler signatures | 94.7% accuracy; stationary humans detectable via 5-12mm breathing displacement | Integrate physical response and GSM-based SOS propagation
02 | Billah et al. (IEEE ICSES, 2024) YOLOv8 Event Detection | Evaluated YOLOv8 nano-to-XL variants at 640×480 on Jetson Nano; 89.4% mAP@0.5 | Camera spray/tamper causes complete detection failure in vision-only systems | Add radar as parallel detection channel independent of optical conditions
03 | Chatterjee et al. (IEEE, 2024) YOLOv8 Intrusion Detection | YOLOv8 perimeter security; MQTT alerts to cloud dashboard; 93.1% day / 81.6% low-light precision | No offline fallback; no physical response; cloud-dependent entire pipeline | Add GSM offline fallback + solenoid lock physical containment layer
04 | Vedrov (IEEE AIoT, 2025) ESP32-CAM + YOLOv8-Nano | Quantized YOLOv5-nano on ESP32-CAM; TFLite inference at 12 FPS / 78.3% accuracy | ESP32 limited by 520KB SRAM — cannot run full YOLOv8 on-chip | Offload vision to RPi Zero 2W; use ESP32 for relay + GSM coordination only
05 | IEEE IoT Journal (2025) Edge Computing on ESP32 | Comparative study of edge inference tasks on ESP32; binary classification <50ms latency | ESP32 viable as coordinator node; unsuitable for full vision inference | Pair with RPi for vision; ESP32 handles sensor fusion + actuation
06 | Hsu et al. (IEEE Sensors Journal, 2023) mmWave Occupancy Estimation | 77GHz radar for indoor people counting; MAE of 0.7 persons in 20m² rooms | Radar-based presence sensing reliable in cluttered environments | Apply to security intrusion detection with physical actuation response
07 | Shen et al. (Sensors, 2024) Fall Detection via 60GHz Radar | CNN on Doppler spectrograms classifies fall vs. normal; healthcare-focused deployment | FMCW radar resolves human body dynamics through clothing at oblique angles | Extend radar fusion concept to security with YOLOv8 visual confirmation

## Slide 8: Literature Survey
Sl. No | Author & Paper Title | Methodology | Learning / Finding | Future Enhancement
08 | Zhang et al. (IEEE JSAC, 2025) 5G mmWave Passive Detection | 5G NR beamforming at 26-28GHz for human presence detection; 87% LoS accuracy | Requires ₹15 lakh per node 5G infrastructure — not embedded feasible | Replace 5G with dedicated ₹450 LD2410 radar per TRAPNET node
09 | IEEE Xplore (2023) IoT Home GSM Alert System | PIR + ESP8266 + SIM900 GSM; SMS alerts over cellular up to 1000km range | Single PIR sensor — misses stationary intruder; no mesh relay or containment | Replace PIR with mmWave; add WiFi beacon + solenoid containment layer
10 | IEEE Xplore (2025) Compact IoT Safety Device | ESP32 + Push button + NEO-6M GPS + GSM; sends location on manual press | Manual activation only — no autonomous detection or physical response | Apply GPS-GSM telemetry to autonomous stolen asset tracking (TRAPNET V2)
11 | IEEE Xplore (2023) Home Security Anti-Theft IoT | PIR + door contact + smoke → MQTT to mobile app over WiFi | Single point of failure: WiFi jammer disables entire system | Add 3-layer offline SOS: WiFi beacon + BLE Eddystone + GSM cellular
12 | IEEE Xplore (2025) Women Safety ESP32+GPS+GSM | ESP32 + NEO-6M + SIM800L; GPS coordinates via SMS on button press | Hardware combination validated at component level for TRAPNET V2 design | Remove manual trigger; add autonomous radar detection before GPS transmit
13 | Devoti et al. (IEEE INFOCOM, 2023) PASID — 5G mmWave Intrusion | Passive intrusion detection via 28GHz 5G AP reflections; no dedicated radar needed | Constrained to environments with 5G mmWave access points — unavailable in target areas | Embed dedicated LD2410 radar eliminating 5G infrastructure dependency
14 | Han et al. (IEEE TMC, 2024) mm-Wave Gait Recognition | 77GHz COTS mmWave + cloud LSTM; 91.3% gait recognition in security corridors | Requires ₹22,000+ radar hardware + cloud connectivity per node | Replace with LD2410 (₹450) + RPi Zero 2W on-device inference; 98% cost reduction
15 | Shahin & Younis (IEEE LCN, 2015) EMC Protocol WiFi-Direct | Proxy-member concept for multi-group WiFi Direct mesh — bridges two peer groups | Proxy-member maps directly to TRAPNET ESP-NOW relay design for building-wide SOS | Apply to TRAPNET multi-node mesh for alert propagation beyond 100m range

## Slide 9
Literature Survey (Continued)
Sl. No | Author & Paper Title | Methodology | Learning / Finding | Future Enhancement
16 | Li et al., IEEE Trans. Ind. Informatics, 2025 — 'Systematic Vital Signs Detection via FMCW MIMO Radar' | FMCW MIMO radar with maximum ratio combining & FastICA for breathing/heartbeat | Validates TRAPNET's LD2410C FMCW micro-Doppler approach for detecting stationary humans | No intrusion response, no door locking, no SOS integration
17 | Chen et al., IEEE Sensors Journal, 2025 — 'Contactless Vital Sign Monitoring on Edge Devices with T-CNN and mmWave' | Low-complexity T-CNN on edge devices for breath/heart rate extraction from FMCW radar | Validates edge deployment of radar processing on resource-constrained devices like ESP32-S3 | Health monitoring only — no security context, no multi-sensor fusion
18 | Russo et al., IEEE Access, 2025 — 'Contactless Monitoring Using Multiple FMCW Radars in 24 GHz Band' | 24GHz FMCW radar with Bayesian filtering for real-time vital sign estimation | Same 24GHz band as TRAPNET's LD2410C; real-time breathing detection validated | No intruder detection logic, no embedded security system
19 | Rahman et al., IEEE ICDEC, 2025 — 'IoT-Enabled Smart Door Lock with RFID, OTP and Intrusion Detection' | ESP32 + RFID + OTP + relay-controlled solenoid lock for smart door security | Same problem — auto door lock on intrusion; validates relay+solenoid approach | PIR only (no radar), no multi-channel SOS, no AI visual confirmation
20 | Ferrag et al., IEEE IoT Journal, 2025 — 'Edge-IIoTset: Comprehensive IoT Cyber Security Dataset' | Edge-based federated learning for IoT intrusion detection at edge nodes | Validates TRAPNET's edge-computing approach with ESP32 + RPi Zero 2W | Cyber intrusion — not physical intrusion; no sensor hardware
21 | Akram et al., IEEE Trans. Consumer Elec., 2024 — 'Secure IoT Smart Home Using Sensor Fusion' | Multi-sensor fusion (PIR + ultrasonic + camera) for false-alarm reduction | Core concept overlap — multi-sensor fusion reduces false positives significantly | No mmWave radar, no trapping, no multi-channel offline SOS
22 | Park et al., IEEE ICIT, 2024 — 'MeshSOS: ESP-NOW Based P2P Emergency Alert Relay System' | ESP32 ESP-NOW peer-to-peer multi-hop relay for infrastructure-free emergency alerts | Directly validates TRAPNET's ESP-NOW mesh relay SOS concept | Worker safety (fall detection) — no intrusion detection, no door locking
23 | Kim et al., IEEE ICCE, 2024 — 'BLE Eddystone Indoor Emergency Notification System' | BLE Eddystone telemetry for passive proximity-based alerts without app installation | Validates TRAPNET's BLE Eddystone SOS broadcast approach | BLE only — no WiFi beacon, no GSM, no ESP-NOW mesh
24 | Wang et al., IEEE AIEC, 2024 — 'Lightweight YOLOv8 on Raspberry Pi for Real-Time Security' | Optimized YOLOv8 (INT8 quantization) on RPi for edge-based person detection | Mirrors TRAPNET's AI pipeline — YOLOv8 on RPi Zero 2W for visual confirmation | Camera only — no radar backup, no physical containment, no multi-SOS
25 | Singh et al., IEEE ICSIC, 2024 — 'IoT Structural Vibration Monitoring for Forced Entry Detection' | Impulse counting with sliding window to distinguish forced entry from ambient noise | Validates TRAPNET's SW-420 vibration sensor pulse-counting approach | Monitoring only — no auto door locking, no radar, no SOS alerts

## Slide 10: Methodology – Four Layer Pipeline Architecture
Pipeline Layer | Hardware & Components | Operational Mechanism & Signal Flow
Layer 1: DETECT (Sensors) | • LD2410C 24GHz mmWave Radar • IR Sensors (Door & Window) • SW-420 Vibration Sensors (x2) • NEO-6M GPS Module • CCTV Camera (RPi CSI) | Fuses radar micro-breathing detection, IR beam-break, vibration triggers, and GPS location tracking. Sends real-time sensor signals to ESP32 coordinator.
Layer 2: PROCESS (Edge-AI Fusion) | • ESP32 DevKit V1 (Main Hub) • Raspberry Pi Zero 2W • Dual LM2596 Bucks (5V / 4V) • 18650 Battery System (TP4056) | ESP32 fuses multi-sensor inputs in <500ms. Raspberry Pi runs OpenCV + YOLOv8 vision AI for secondary confirmation over MQTT Serial bridge to prevent false alarms.
Layer 3: RESPOND (Actuation & Log) | • 2-Ch Relay Module (Active-LOW) • 12V Solenoid Door Lock • MicroSD Card Module (16GB) • 0.96 inch OLED Display (SSD1306) | Relay triggers 12V solenoid lock within 3s upon threat confirmation to trap intruder. System status displayed on OLED HUD; events logged to FAT32 MicroSD.
Layer 4: ALERT (Multi-Layer SOS) | • SIM800L GSM Module (+1000uF cap) • Onboard ESP32 Radios (WiFi Beacon + BLE + ESP-NOW) | Sends GSM SMS alerts to owner & police via SIM800L. Simultaneously broadcasts WiFi Beacon SSID (30m), BLE Eddystone (15m), and ESP-NOW Mesh Relay (200m+). Zero internet required.

## Slide 11: Justification of Methodology
Design Choice / Methodology | Why This Method Was Selected | Alternatives Rejected & Why
Four-Layer Pipeline (Detect-Process-Respond-Alert) | Decouples sensing, processing, actuation & alert into modular layers. Multi-sensor fusion (radar+IR+vibration+camera) reduces false alarms to near zero. | Single-layer monolithic architecture (unstable, single point of failure); PIR-only motion sensing (misses stationary intruders).
mmWave Radar (LD2410C 24GHz, ~Rs450) | Detects 5mm chest breathing motion of stationary/hidden humans via micro-Doppler signatures. Works through light obstacles. | PIR sensor (misses frozen intruder); 77GHz COTS radar (Rs22,000+); UWB radar (Rs40,000+ per node - cost prohibitive).
Dual-Controller Fusion (ESP32-S3 + RPi Zero 2W) | ESP32-S3 acts as <500ms hard real-time coordinator. RPi Zero 2W handles heavy YOLOv8 Edge-AI vision confirmation over MQTT Serial bridge. | ESP32-CAM TFLite (low accuracy, poor resolution); Jetson Nano (Rs15,000+ - over budget); Cloud AI (requires internet).
Solenoid Door Lock (12V, <3s Containment) | Physically contains intruder in <3 seconds, directly solving the core 'record-only' limitation of standard CCTV security systems. | Alarm sirens alone (thief ignores and flees); Fog machines (hazard/maintenance issues); CCTV alert only (no physical protection).
Multi-Layer SOS (GSM + WiFi + BLE + ESP-NOW) | 4 redundant channels ensure alert delivery during WiFi jamming or power cuts. GSM SMS reaches phone 99.9%; BLE/WiFi beacon needs no app; ESP-NOW relays 200m+. | Single WiFi/App alert (disabled by Rs200 jammer); Siren-only (no remote notification); LTE-M per node (high monthly SIM cost).
Dual-Rail Power (LM2596 Bucks + 18650s) | Dedicated 4V buck + 1000uF cap absorbs SIM800L 2A transmit spikes without ESP32-S3 brownout. 18650 battery backup provides 4-6 hrs operation. | Single 5V rail (SIM800L current bursts reset ESP32); Lead-acid UPS (heavy, bulky); No battery backup (mains wire cut disables system).
MicroSD Evidence Log (16GB FAT32 SPI) | Provides tamper-proof, timestamped local event logging independent of cloud connectivity or internet uptime. | Cloud-only storage (fails during internet outage or jamming); Internal RAM buffer (event data lost on power reset).

## Slide 12
Proposed Block Diagram
Tamper-Resilient mm Wave-Radar-Based Intrusion Containment System with Mesh-Relayed SOS Alerts

## Slide 13
Component List & Hardware Specifications
Status | Component | Model / Specification | Qty | Interface & Purpose
☐ | Main MCU | ESP32 DevKit V1 (WROOM-32) | 1 | V1 Basic Coordinator; Sensor Fusion + SOS; WiFi/BLE
☐ | Human Radar | LD2410C (24GHz mmWave) | 1 | UART2 (256000 baud); 5mm breathing motion detect
☐ | IR Obstacle Sensor | FC-51 / HW-201 | 2 | Digital GPIO (GPIO4, 13); door & window breach
☐ | Vibration Sensor | SW-420 (Adj. sensitivity) | 2 | Digital GPIO (GPIO34, 39 + 10kohm pull-down); forced entry
☐ | GPS Module | NEO-6M (GY-GPS6MV2) | 1 | SoftSerial (9600 baud); location tracking for SOS
☐ | CCTV Camera | RPi Camera Module V2 / USB | 1 | CSI / USB to RPi; visual person detection
☐ | AI Processor | Raspberry Pi Zero 2W | 1 | UART (115200 baud) to ESP32; OpenCV + YOLOv8
☐ | Buck Converter #1 | LM2596 DC-DC Step-Down | 1 | 12V -> 5.0V output rail for ESP32, LD2410, Relay, RPi
☐ | Buck Converter #2 | LM2596 DC-DC Step-Down | 1 | 12V -> 4.0V dedicated output rail for SIM800L GSM
☐ | Battery Backup | 18650 Li-Ion (x2) + TP4056 | 1 set | 7.4V power backup (4-6 hours operation during outage)
☐ | Relay Module | 2-Ch 5V Opto-Isolated | 1 | Digital GPIO (GPIO32/33, Active-LOW); 12V lock switch
☐ | Solenoid Lock | 12V Electromagnetic Lock | 1 | 12V direct via relay; <3s physical intruder containment
☐ | MicroSD Module | SPI Breakout + 16GB Card | 1 | VSPI Bus (GPIO18/19/23/15); local FAT32 evidence log
☐ | OLED Display | 0.96 inch SSD1306 (128x64) | 1 | I2C (GPIO21/22, Addr: 0x3C); real-time HUD status
 | Main MCU | ESP32-S3 DevKit V1 (WROOM-N16R8) | 1 | V2 Advanced Upgrade: Vector AI instruction, Dual Type-C, USB-OTG

## Slide 14: Conference Certificate
Paper Submission & Acceptance
Project Title:
“Design and Implementation of a Tamper-Resilient mm Wave-Radar-Based Intrusion Containment System with Mesh-Relayed SOS Alerts”
Institution: Sathyabama Institute of Science and Technology
Department: Electronics and Communication Engineering
[ Conference Certificate Image ]
[ Conference Proceedings Cover Page Image ]
(Replace the placeholder text above with your actual certificate images)